## Slide 1: X115 – Hallfield Estate (Lynton House, Worcester House & Winchester House) Resident Meeting
8th June 2022

## Slide 2: Contents
Asset Strategy Team Introduction
Works Programme Summary
Proposed Scope of Works
Next steps

## Slide 3: Asset Team Introduction
Responsible for all planned major works in Westminster.
Works and justification identified and prioritised through stock condition information held on Keystone database, in-house and independent condition surveys, reports and referrals from WCC Housing Management Teams, ASB Teams, Ward Councillors, Met Police etc.
Produce client briefs for all major works.
Responsible for briefing the Term Partnering Contractors.
Gaining all stakeholder sign-offs and pass to the commissioning team.

## Slide 4: Works Programme Summary
  Stage 1 – Client brief (resident intro meeting)
  Stage 2 – Client brief issue to Commissioning Team & TPC
  Stage 3 – Project execution plan (resident PEP review meeting)
  Stage 4 – Pre-commencement order and detailed design stage
  (resident SPP review meeting)
  Stage 5 – Commencement order and mobilisation stage (meet the contractor session)
  Stage 6 – Contract period
  Stage 7 – Completion and defects period
  Stage 8 – End of defects sign off

## Slide 5: Scope of Works
Item | Works Required & Justification
Window Replacement | The windows throughout all blocks are defective and considered to be beyond economical repair and will be replaced. New replacements to match existing windows seen under previous phases (Smart Architectural Aluminium Windows). Works will also include for integrated door screen and balconies. Making good to disturbed areas around windows as a result of window installation works. Redecoration and repair as required.
External and Internal Repairs and Redecorations | Cleaning and localised repairs to render, concrete, brick, stone, metalwork and pointing: cracking, spalling and staining is visible to the building fabric. Full internal and external decoration and cleaning to blocks. Replacement of defective and damaged external cladding tiles to Winchester House. New soffit insulation to undercroft areas.
Mechanical & Electrical | The lateral mains, including distribution boards and landlord lighting supply are at the end of their current lifecycle and will need to be replaced. Replacement of communal lighting to stairwells and walkways.

## Slide 6: Scope of Works - continued
Item | Works Required & Justification
Fire Safety Works | To comply with current building/fire regulations – All internal communal escape areas, including corridors and staircase areas will be redecorated to achieve a class ‘0’ paint compliant finish. Fire stopping included for any potential compartmentation breaches e.g. through floor service penetrations or new ducting.
Door Replacements | Replacement of tenant flat entrance doors (lessees on an opt-in basis) and internal communal doors to modern fire door standards. Required to comply with current building/fire regulations and create a safe route of exit for residents in an emergency. Replacement of defective communal doors e.g. tank room doors and bin store doors.
Walkways | Asphalt repairs to communal walkways
Environmental Works | As part of Westminster’s commitment to reduce properties affected by condensation and mould, new extractor fans will be fitted to tenanted properties kitchens and bathrooms where required.

## Slide 7
Timetable
The next steps will be:
  September ‘20
  *These dates may be subject to change.
Milestone | Estimated dates*
Internal approval and sign off | Summer 2022
Issue client brief to contractor for design stage | Summer 2022
Planning application submission | Autumn 2022
NOE consultation period | Spring 2023
Contractor mobilisation | Summer 2023
Start on site | Early Autumn 2023

## Slide 8
Questions?